## Slide 1
Maxim Titov, CEA Saclay, France
« Development of Micro-Pattern
Gaseous Detector Technologies »
and the RD51 Collaboration
MM for ATLAS upgrade
THGEM for COMPASS
upgrade
GEM for CMS upgrade
GEM for ALICE TPC
upgrade
Joint Instrumentation Seminar, DESY/Hamburg, September 4, 2015
OUTLINE of the TALK:
Introduction: Major Micro-Pattern gas Detector Technologies
(GEM, Micromegas, Thick GEM, InGrid, mPIC)
Summary of the RD51 – MPGD Technology Highlights
(Large area MPGDs - Support of HL- HLC Upgrades, R&D (quality control, long-term tests), Academia-Industry Matching Event, Software & Simulation, SRS Electronics, CERN MPGD Production Facility & Industrialization, RD51 Test Beam Facility, Training)

## Slide 2
History of Gaseous Detector Developments
M. Hoch, 2004 Wire Chamber Conference

## Slide 3
Multi-Wire Proportional Chamber (MWPC)
Gaseous proportional tracking detectors that revolutionized High Energy Physics
With Fabio Sauli et Jean Claude Santiard
The 1st “Large Wire Chamber”…
Georges Charpak
1924 – 2010
The invention revolutionized
particle detection, which
passed from the manual
to the electronic era.

## Slide 4
Nobel Prize: W, Z - Discovery at UA1/UA2 (1983)
UA1 used the largest imaging drift chamber of its day (5.8 m long, 2.3 m in diameter)
It can now be seen in the CERN Microcosm Exhibition
Z  ee (white tracks)
Particle trajectories in the CERN-UA1
3D Wire Chamber
Discovery of W and Z bosons
C. Rubbia & S. Van der Meer
Nobel Prize 1984

## Slide 5
Gaseous Detectors in LHC Experiments
 | Vertex | Inner Tracker | PID/ photo- det. | EM CALO | HAD CALO | MUON Track | MUON Trigger
ATLAS | - | TRD (straws) | - | - | - | MDT (drift tubes), CSC | RPC, TGC (thin gap chambers)
CMS TOTEM | - | - | - | - | - | Drift tubes, CSC, GEM | RPC, CSC GEM
LHCb | - | Straw Tubes | - | - | - | MWPC | MWPC, GEM
ALICE | - | TPC (MWPC) | TOF(MRPC), PMD, HPMID (RICH-pad chamber), TRD (MWPC) | - | - | Muon pad chambers | RPC
ALICE TPC
Straw tubes
CMS CSC
Gaseous detectors are still the first choice whenever the large-area coverage (e.g. muon systems) with low material budget is required

## Slide 6
ALICE Multi-Gap RPC: Timing Resolution
Relevant scale in HEP: t ~ L(m)/c ~ o(ns)
Traditional technique:
  Scintillator + PMT ~ o (100 psec)
Breakthrough with a spark discharge in gas
  Pestov counter  ALICE MRPC ~ 50psec
Multi-Gap Resistive Plate Chamber: Basic Principle
Technology | Time resolution
Pestov Counter | 30-50 ps
RPC | ~ 1-5 ns (MIP)
MultiGap RPC | ~ 50 ps (MIP)
GEM | ~ 1-2 ns (UV) ~ 5 ns (MIP)
Micromegas | ~ 700 ps (UV) ~ 2-5 ns (MIP)
C. Williams, CERN Detector Seminar
“ALICE Time of Flight Detectors”: http://indico.cern.ch/conference
Display.py?confId=149006

## Slide 7
ALICE Multi-Gap RPC: Timing Resolution
Relevant scale in HEP: t ~ L(m)/c ~ o(ns)
Traditional technique:
  Scintillator + PMT ~ o (100 psec)
Breakthrough with a spark discharge in gas
  Pestov counter  ALICE MRPC ~ 50psec
Technology | Time resolution
Pestov Counter | 30-50 ps
RPC | ~ 1-5 ns (MIP)
MultiGap RPC | < 50 ps (MIP)
GEM | < 1-2 ns (UV) ~ 5 ns (MIP)
Micromegas | < 700 ps (UV) ~ 2-5 ns (MIP)
C. Williams, CERN Detector Seminar
“ALICE Time of Flight Detectors”: http://indico.cern.ch/conference
Display.py?confId=149006
ALICE-TOF has 10 gaps (two stacks of 5 gas gaps);
each gap is 250 micron wide

## Slide 8
Gaseous Detector Systems for the High-Luminosity LHC
ATLAS TGC
LHCb Outer
Tracker
ALICE MRPC
ALICE HPMID
Upgrade Options for HL-LHC:

## Slide 9
INSTRUMENTATION FRONTIER:
DEVELOPMENT OF MICRO-PATTERN
GASEOUS DETECTOR TECHNOLOGIES
Detector –Electronics Integration  Enabled by Advanced Technologies
(better granularity / high precision / small amount of material)
Modern photo-lithography technology  Micro-Pattern Gas Detectors
Microelectronics – eg. Silicon pixels
Bump bonding technology – low capacitance connections
Trade-offs between high-speed, power, S/N, integration, segmentation, radiation tolerance  defined by the state-of-the-art in microelectronics
50 mm
140 mm
Micromegas:
10 mm
100 mm
Ingrid
High Rates & enormous occupancy:
Silicon detectors:
Si-strips Pixel (2D) 3D detectors
& 3D TSV integration
Gaseous detectors:
Wire Chamber  Wireless MPGD (2D)  InGrid/Timepix (3D)
MSGC:

## Slide 10
Christian Lippmann, 2nd ECFA High Luminosity LHC Experiments
Workshop, Aix-les-bains, France, October 21-23 (2014)

## Slide 11
Micromegas
GEM
Thick-GEM, Hole-Type and RETGEM
MPDG with CMOS pixel ASICs (“InGrid”)
Micro-Pixel Chamber (mPIC)
Electrons
Ions
60 %
40 %
Micromegas
GEM
THGEM
MHSP
InGrid
Micro-Pattern Gaseous Detector Technologies for Future Physics Projects
mPIC
Rate Capability:
MWPC vs MSGC

## Slide 12
GEM (Gas Electron Multiplier)
Thin metal-coated polymer foil chemically pierced by a high density of holes
Electrons are collected on patterned
readout board.
A fast signal can be detected on the lower
GEM electrode for triggering or energy
discrimination.
All readout electrodes are at ground potential.
S1
S2
S3
S4
Induction gap
e-
e-
I+
F. Sauli, Nucl. Instrum. Methods A386(1997)531
F. Sauli, http://www.cern.ch/GDD
A difference of potentials of ~ 500V is
applied between the two GEM electrodes.
the primary electrons released by the
ionizing particle, drift towards the holes
where the high electric field triggers the
electron multiplication process.

## Slide 13
MPGD Simulation Tools (Avalanche Simulation in GEM)
Animation of the avalanche process
(monitor in ns-time electron/ion
drifting and multiplication in GEM):
electrons are blue, ions are red, the
GEM mesh is orange
ANSYS: field model
Magboltz 8.9.6: relevant
cross sections of electron-matter interactions
Garfeld++: simulate
electron avalanches
http://cern.ch/garfieldpp/examples/gemgain

## Slide 14
Gas Electron Multiplier (GEM)
F. Sauli, NIM A386(1997) 531;
F. Sauli, http://www.cern.ch/GDD
Full decoupling of amplification stage (GEM)
and readout stage (PCB, anode)
Cartesian
Compass, LHCb
Small angle
Hexaboard, pads
MICE
Mixed
Totem
2009: NEW: Single mask GEM production technique 
allow to extend GEM foils to ~ m2 area
2009:
1996:

## Slide 15
MICro MEsh GAseous Structure (MICROMEGAS)
Y. Giomataris et al, NIM A376(1996)29
Micromesh Gaseous Chamber:
micromesh supported
by 50-100 mm insulating pillars
Multiplication (up to 105 or more)
takes place between the anode and
the mesh and the charge is collected
on the anode (one stage)
Small gap: fast collection of ions

## Slide 16
Standard vs Resistive Micromegas Sparking
Standard MM could not be operated in neutron beam
HV break-down and currents > several µA for gains ~ 1000–2000
MM with resistive strips worked perfectly well
No HV drops, small spark currents up to gains of 2 x 104
Standard MM
Resistive MM
Since 2010: Resistive Micromeas technology
Problem was solved by adding a layer of resistive strips above the readout strips
Spark neutralization/suppression
(sparks still occur but become inoffensive)

## Slide 17
« MicroBulk » Micromegas

## Slide 18
INSTRUMENTATION FRONTIER:
PIXEL READOUT OF MPGDs –
Ultimate Gas-Silicon Detector Integration
Ingrid
Triple GEM stack + Timepix ASIC (5 GeV e-):
1.5 cm
“Octopuce” (8 Timepix ASICs):
X-Rays
a-particles

## Slide 19
“InGrid”:
Protection Layer (few mm)
against sparks
~ 50 mm
Medipix2 / Timepix ASIC
“InGrid” Concept: By means of advanced wafer processing-technology INTEGRATE
MICROMEGAS amplification grid directly on top of CMOS (“Timepix”) ASIC
3D Gaseous Pixel Detector  2D (pixel dimensions) x 1D (drift time)
Pixel Readout of MPGDs: “InGrid” Concept

## Slide 20
“InGrid’ Technology and “Driving” Developments
Since 2011: Major Step Forward 
InGrid Production on a wafer level (107 chips)
2005: Single “InGrid” Production
2009: “InGrid” Production on a
3 x 3 Timepix Matrix

## Slide 21
Photosensitive Detector: Integrating Ingrid and CMOS readout
MICROMEGAS (InGrid)
covered with CsI
photon
CsI PC
Chip area: 14x14mm2.
(256×256 pixels of 55×55 μm2)
Chip area: 14x14mm2.
(256×256 pixels of 55×55 μm2)
TIMEPIX:
Ingrid without CsI
Ingrid with CsI PC:
2D UV Image
of a 10mm
diameter mask
UV absorbed
by the
fingerprint
on the window
M. Fransen, RD51 Mini-Week, Sep. 23-25, 2009, WG2 Meeting

## Slide 22
MPGD-Based Gaseous Photomultipliers (GPM)
Multi-GEM Gaseous Photomultipliers:
Largely reduced photon feedback
(can operate in pure noble gas & CF4)
Fast signals [ns]  good timing
Excellent localization response
Able to operate at cryogenic T
CsI ~ 500 A
Semitransparent
Photocathode (PC)
CF4
770 torr
3 GEM
s = 1.6 ns
Single Photon Time Resolution:
CsI ~2500 A
Reflective
Photocathode (PC)
200 µm
FWHM ~160 µm
Beam ~ 100 µm
Intrinsic accuracy
s (RMS) ~ 55 µm
Single Photon Position Accuracy:
E.Nappi, NIMA471 (2001) 18; T. Meinschad et al, NIM A535 (2004) 324; D.Mormann et al., NIMA504 (2003) 93
Micromegas: s ~ 0.7 ns with MIPs
GEM Gaseous Photomultipliers (GEM+CsI photocathode) to detect single photoelectrons

## Slide 23
1,0E-02
1,0E-01
1,0E+00
1,0E+01
1,0E+02
1,0E+03
1,0E+04
1,0E+05
1,0E+06
1,0E+07
0
200
400
600
800
1000
D
V THGEM (V)
Gain
MM = 330 NeCF4 10%
MM = 290 NeCF4 5%
DTHGEM NeCF4 10%
DTHGEM NeCF4 5%
Thick-GEM Multipliers (THGEM)
STANDARD GEM
103 GAIN IN SINGLE GEM
THGEM
105 gain in single-THGEM
1 mm
0.1 mm rim
to prevent
discharges
Simple & Robust  Manufactured by standard PCB techniques
of precise drilling in G-10 (and other materials) and Cu etching
Other groups developed
similar hole-multipliers:
Optimized GEM:
L. Periale et al.,
NIM A478 (2002) 377.
LEM: P. Jeanneret,
PhD thesis, 2001.
Effective single-electron detection
(high gas gain ~105 (>106) @
single (double) THGEM)
Few-ns RMS time resolution
Sub-mm position resolution
MHz/mm2 rate capability
Cryogenic operation: OK
Gas: molecular and noble gases
Pressure: 1mbar - few bar
106
C. Azevedo et al.; arXiv: 0909.3191
Double THGEM or THGEM/Micromegas

## Slide 24
THGEM Photon Detectors for RICH: Efficiency Evaluation
Azevedo et al., arXiv:0909.5357
PE efficiency
extraction
into the gas
vs vacuum:
Single PE
collection efficiency
into THGEM holes:

## Slide 25
A.Buzulutskov et al, IEEE TNS 50 (2003) 2491;
A.Bondar et al, NIMA 524 (2004) 130
A.Bondar et al, NIMA 556 (2006) 273
A.Rubbia, J. Phys. Conf. Ser. 39 (2006) 129
A.Buzulutskov, A.Bondar, JINST 1 (2006) P08006
Y.L.Ju et al, Cryogenics 47 (2007) 81
A. Bondar et al, JINST 5 (2010) P08002
A.Buzulutskov et al, EPL 94 (2011) 52001
L.Periale et al, IEEE TNS 52 (2005) 927
M.Gai et al, Eprint arxiv:0706.1106 (2007)
D.Akimov et al, JINST 4 (2009) P06010
A.Bondar et al, JINST 3 (2008) P07001
P.K.Lightfoot et al, JINST 4 (2009) P04002
N.McConkey et al, IPRD 2010, Siena, Italy; Nucl. Phys. B Proc. Suppl. 215 (2011) 255
D.Akimov, NIMA 628 (2011) 50
S. Duval et al, JINST 6 (2011) P04007
S. Duval et al, JINST 4 (2009) P12008
MPGD-Based Cryogenic Avalanche Detectors: Concept Gallery

## Slide 26
Micro-Pixel Chamber (mPIC) at Kobe University
m-PIC：micro pixel gas chamber
Area: 10x10cm – 30x30cm
Readout pitch :400μm
Production using PCB technology
Invented by A.Ochi, T.Tanimori (NIMA471 (2001) 264)
Application: X-ray imaging, Gamma camera,
Medical RI tracing
NEW: m-PIC design with resistive
cathode:
Cathode patterns are formed by resistive material.
Large current from spark reduce the e-field, and spark will be quenched.
This design provide one promising possibility of MIP detector under hadronic background
Surface pictures of resistive mPIC:

## Slide 27
High Rate Capability
High Gain
High Space Resolution
Good Time Resolution
Good Energy Resolution
Excellent Radiation
Hardness
Ion Backflow Reduction
Photon Feedback
Reduction
Micromegas
GEM
Micromegas
2x106 Hz/mm2
GEM
GEM
Why Micro-Pattern Gaseous Detectors are so attractive …
s time ~ few ns
sspace ~ 15-40 mm
One of the recent reviews describing
the progress of the RD51 collaboration:

## Slide 28
1988
MSGC (ILL, A. Oed)
GEM (CERN, F. Sauli)
1996
MicroMEGAS (CEA Saclay, Y. Giomataris)
1997
2000
m-PIC (A. Ochi, T. Tanimori)
Capillary plate (Yamagata U., H. Sakurai)
1996
2005
2008
RD51
collaboration
InGrid
RD28
1992
Historical Roadmap of the MPGD Technologies and RD51 Collaboration
2003
LEM (Periale)
THGEM(Chechik)
Many of the Micro-Pattern Gaseous Detector Technologies were introduced before
the RD51 Collaboration was founded
With more techniques becoming available (or affordable), new detection concepts
are being introduced and the existing ones are substantially improved

## Slide 29
More than 80 groups
More than 400 people
National and International Laboratories
National Institutes and Universities
The main objective is to advance MPGD technological development and associated electronic-readout systems, for applications in basic and applied research”: http://rd51-public.web.cern.ch/rd51-public
10
3
58
15
Large Scale R&D program to advance MPGD Technologies
Access to the MPGD “know- how”
Foster Industrial Production

## Slide 30
Summary of the RD51 Achievements (2008 – 2013)
Consolidation of the Collaboration and MPGD Community Integration (> 80 institutes, 450 members);
Major progress in MPGD Technologies: Large area GEM (single mask), Micromegas (resistive) and THGEM; picked up by experiments, including LHC upgrades;
Secured future of the MPGD Technologies development through the TE MPE workshop upgrade and FP7 AIDA contribution
Contacts with industry for large volume production; MPGD industrialization and first industrial runs
Major improvement to the MPGD simulation software framework for small-scale structures for applications;
Development of common, scalable readout electronics (SRS); many developers and > 50 user groups; Production (PRISMA company and availability through CERN store); Industrialization (re-design of SRS in ATCA in EISYS)
Infrastructure for common RD51 test beam and facilities (> 20 user groups);

## Slide 31
RD51
Large Area Detectors
Assembly Optimization
RD51 Common Projects
Generic R&D, QA
Long Term Stability
Software Tools and
Simulations
MPGD Electronics
CERN MPGD
Workshop,
Quality Control
and Industrialization
RD51 Common
Test Beam and Lab Facilities
WG5:
WG4:
WG1:
WG2:
WG7:
WG6:
Conferences / Schools
Academia-Industry
Matching Events
Future RD51 Collaboration Activities (beyond 2013)
WG3/NEW WG:

## Slide 32
MPGD Technologies for Energy Frontier (HL-LHC, LC)
 | Vertex | Inner Tracker | PID/ photo- det. | EM CALO | HAD CALO | MUON Tracking | MUON Trigger
ATLAS |  |  |  |  |  | Micromegas | Micromegas
CMS TOTEM |  |  |  |  | Backing-HE (GEM, MM) | GEM GEM | GEM GEM
LHCb |  |  |  |  |  |  | GEM
ALICE |  | TPC (GEM) |  |  |  |  | 
Linear Collider |  | TPC(MM,GEM, InGrid) |  |  | DHCAL(MM,GEM,THGEM) |  | 
ATLAS Micromegas:
On a road to large-area detectors:
(1.2 * 0.6 m2)
CMS GEM:
Trapezoidal GEM Prototype (99 x 45-22 cm2)

## Slide 33
ALICE (GEM)
ATLAS NSW (Micromegas)
LHC Upgrades: Original R&D efforts emerged from RD51 activities.
Today: production phase under the project effort , access to RD51 facilities (laboratory, test beam, workshops) and tools (simulation, electronics,…) to facilitate this particular phase
Elba 2015
Elba 2015
WG1: Examples of CERN/LHC Upgrades (“large achievement for MPGD community”)

## Slide 34
WG1: Examples of CERN/LHC Upgrades (“large achievement for MPGD community”)
CMS (GEM)
COMPASS RICH-1 (THGEM+MM)
Elba 2015
Elba 2015
LHC Upgrades: Original R&D efforts emerged from RD51 activities.
Today: production phase under the project effort , access to RD51 facilities (laboratory, test beam, workshops) and tools (simulation, electronics,…) to facilitate this particular phase

## Slide 35
Range of track angles in NSW
Resistive Micromegas Performace: Resolution vs Track Angle
Using charge amplitude (Centroid hit)
Spatial resolution rapidly decreases for inclined
tracks if the cluster centroid (e.g., charge weighting)
is used; small strip pitch does not help
Using time information (TPC segment)
Measuring the arrival time of the signals opens a new dimension; in this case the MM functions like a TPC
=> Track vectors/plane for inclined tracks
Combination of centroid & TPC 
spatial resolution < 100 mm independently of track incident angle !
Spatial resolution vs magnetic field:
J. Wotschack

## Slide 36
Stress and deflection test
Test of segmented FR4 skin glueing with different stiffeners
Will serve for deformation studies
3.7 m
1.8 m
Micromegas for ATLAS NSW: Full Sector Mechanical Prototype (CERN)
J. Wotschack

## Slide 37
2010
Generation I
The first 1m-class detector ever built but still with spacer ribs and only 8 sectors total. Ref.: 2010 IEEE (also RD51-Note-2010-005)
2011
Generation II
First large detector with 24 readout sectors (3x8) and 3/1/2/1 gaps but still with spacers and all glued. Ref.: 2011 IEEE. Also RD51-Note-2011-013.
2012
Generation III
The first sans-spacer detector, but with the outer frame still glued to the drift.
Ref.: 2012 IEEE N14-137.
2013
Generation IV
First detector with complete mechanical assembly; no more gluing parts together!
MPGD 2013;
and IEEE2013.
2014
Generation V
Nearly final CMS
design: stretching apparatus that is now totally inside gas volume. Ongoing test beam campaign for final performance measurements.
2014/2015
Generation VI
Latest detector design; to be installed in CMS. Optimized final dimensions for max. acceptance and final eta segmentation. Ongoing test beam campaign for DAQ
GEM foil production uses single mask technology for wet etching
  Dramatically reduces foil production costs and allows large sizes to be manufactured
NS2 assembly technique developed
  Construction time reduced from week(s) to two hours per chamber
GEM Technology: From GE 1/1 to GE1/1-v6 Prototypes
A. Sharma

## Slide 38
Consolidation of existing structures: Cylindrical MPGDs as an example
E. Oliveri

## Slide 39
MPGD Readout for the Time Projection Chamber at the ILC/CLIC
MPGDs are foreseen as TPC readout for ILC
or CLIC (size of endcaps of ~ 10 m2):
Standard “pad readout” (1x 6 mm2): 8 rows of det. modules (17×23 cm2); 240 modules per endcap
“Pixel readout” (55x 55mm2): ~100-120 chips per module → 25000-30000 per endcap
Backgrounds in
CLIC TPC requires
very small pixels
(< 1x1 mm2)
CLIC TPC
Simulation
(M. Killenberg)
ILCTPC with MPGD-Readout:
(spatial resolution < 100 mm @ 5T)
Laser-etched GEMs 100µm thick (‘Asian GEMs’)
Wet-etched triple GEMs
Resistive MM with dispersive anode
GEM + pixel readout
InGrid (integrated Micromegas grid with pixel readout)

## Slide 40
MPGD-based “Pad Readout” for ILC TPC
Diameter 77cm
Large TPC Prototype with versatile endplate @ DESY
Efforts to improve the modules design for all technologies. Several test beams campaigns:
7 Micromegas modules with 2-phase C02 cooling
With beam and laser dots:
UV laser gererates MIP tracks
& illuminate calibration spots
2P CO2
Cooling
MM (B=0): Before correction
Goal for final TPC can be reached:
GEM / MM performance similar
MM (B=0): After correction
(note – different scale)

## Slide 41
MPGD-based “Pixel Readout” for ILC TPC
LARGE AREA: 160 InGrid detector setup
 3 modules: 1 x 96 InGrid, 2 x 24 InGrids
 Readout 5 SRS FECs
By design:
Singe electron detection
Time-of-arrival measurement
High granularity; Uniform gas gain
Module with
96 InGrids
on 12 „octoboards“
24 InGrid installation in LP
LP endplate with 3 modules
Preliminary data analysis:
Track reconstruction
→ straight and curved tracks
→ ≈ 3000 hits per 50 cm track
Physics properties of the TPC
→ field distortions; reliability
→ dE/dx resolution;delta identification
→ single point resolution
→ momentum measurement
M. Lupberger

## Slide 42
COMPASS RICH I Upgrade: Long-Term Experience, Performance
PMTs not adequate because of large angular acceptance  only small demagnification
factor of optical system allowed (large distortions); 5 m2 of PMTs not affordable.
COMPASS RICH I:
UPGRADE OF COMPASS RICH I:
1999-2000: 8 MWPC with CsI (RD26 @ CERN)
After a long-term fight for increasing electrical stability
at high rates: robust operation is not possible at gain~105 because of photon feedback, space charge & sparks
MPGD-Photon Detectors are the best option
beam off: stable
operation up to > 2300 V
beam on: stable operation
possible only up to ~2000 V
2006: 4 central CsI+cathodes:
remove and insert frames with
MAPMTs and lense telescopes
PMTs not adequate  only small demagnification
factor allowed; 5 m2 of PMTs not affordable.
 Micromegas +THGEM, the hybrid architecture
structure, is one of the most advanced scheme:
Higher performance reached with the MM + THGEM
architecture (than multiple-THGEM structures)
F. Tessarotto

## Slide 43
LEM (THGEM) Technology for Double Phase Ar-TPC
Double-phase Ar LEM TPC

## Slide 44
Calorimetry with MPGD:
Fast Timing:
Resistive Material:
Preliminary
Elba 2015
Elba 2015
O8/2014 KUBEC Workshop
≈50phe
≈50phe
Elba 2015
New Materials (Glass GEM):
O2/2015
The Latest Results of Crystalized Glass GEM, Y. Mitsuia, RD51 miniweek (GDD/RD51 lab)
B10
Gd
Neutrons Detection:
European Spallation Source (ESS)
O3/2015
Large Area Thin Detectors:
WG2: Generic R&D, Examples of New Ideas, Applications
E. Oliveri

## Slide 45
Preliminary
≈50phe
≈50phe
FAST-TIMING MPGDs on MM concept:
WG2: Generic R&D, Examples of New Ideas
Convert single-photoelectron time jitter
of a few hundred picoseconds into an incident-particle timing response of the order of 50 ps
S. White, DESY Seminar,
June 12, 2015
Study of charge-transfer properties through
graphene for gas detector applications:
Elba 2015
F. Resnati

## Slide 46
Star
Mirror
Snake
Real R1 values:
400 -750 KOhms
with 100KΩ/Sq
Real R1 values:
4 MOhms with 100KΩ/Sq
Real R1 values:
40 MOhms With 100KΩ/Sq
Work by LAPP Annecy, NCSR Demokritos , Univesrity of Athens, CEA IRFU
M. Chefdeville, T. Geralis
Optimisation:
 reduce resistivity
and evacuation time
but still suppress sparking
– “Vertical” evacuation
of charge using buried
resistors, proposed
by Rui de Oliveira
– Ongoing program:
Vary the RC, measure
the linearity (rate &
dE/dx scans),
check sparking
RESISTIVE MICROMEGAS: Resistive layers are known to quench sparks at early stage
  “Horizontal” evacuation of charge  might be too slow for large areas
  Segmented R-layer to limit physical crosstalk
WG2: Generic R&D, Tracking/Calorimetry Applications

## Slide 47
Electrical rigidity
Hole diameter uniformity in GEM
Gap uniformity in MicroMegas
THGEM thickness uniformity
Final detector calibration and characterization protocols and infrastructure
WG2: R&D Continuation - Quality Control

## Slide 48
Classical gas detectors ageing detector
Radiation hardness and activation of detector components
Sustainability to neutrons and heavily ionizing particles induced discharges
Exposure to X-Ray, Gamma, Neutron and Alpha Sources
Monitoring infrastructure
Resistive MicroMegas
stability performance
under X-Ray irradiation
Discharge studies of the triple GEM detector exposed to the low energy neutron flux
Portable gas monitoring
system for detector stability
studies
 to be used by LHCb and
CMS upgrade for the
muon system
WG2: Radiation Hardness Studies - Long Term Stability
Radiation hardness of MPGDs is comparable with solid-state
Sensors in harsh radiation environments
 still, it is important to develop and validate materials
with resistance to ageing and radiation damage.

## Slide 49
https://indico.cern.ch/event/365840/
https://indico.cern.ch/event/392833/
https://indico.cern.ch/event/265187/
Summary (arXiv 1410.1070)
Press release
(understanding requirements, applications, approaching new communities and technologies)
Photon Detection
Neutron Detection 1st
Neutron Detection 2nd
16-17 March 2015
10-11 June 2015
14-15 October 2013
Platform: Research + industry + potential users to foster collaboration on dedicated applications
WG3: RD51 Academia – Industry Matching Events

## Slide 50
WG3: RD51 Academia – Industry Matching Events: Neutrons & MPGDs
A large Community - Strong interaction with RD51
Use of MPGD Detector R&D, tools and electronics (RD51 SRS & ATLAS NSW VMM)
There is tangible mutual interest between the HEP and neutron-scattering communities
to advance the technology of MPGDs:
GEM-based solutions for thermal-neutron detection at spallation sources,
novel high-resolution neutron devices for macromolecular crystallography,
fast neutron MPGD detectors in the fusion
represent a new frontier for future developments.

## Slide 51
RD51 participated in XII ICFA School (Bogota, Colombia)
2014 (Novi Sad)
2011
2013
2013
2009
RD51 Organized Events:
MPGD assembly
RD51 participated in Danube School on Instrumentation (Novi Sad Serbia)
RD51 MPGD Lectures:
  MPGD students lectures (1 week) at the International Workshop on Advance Detectors & RD51 CM in Kolkata
October 2014
WG3: RD51 Collaboration & International Schools
MPGD simulation
MPGD electronics
The vitality of the MPGD community
resides in the relatively large number
of young scientists
educational events constitute an
important activity.

## Slide 52
RD51
Cosmic Ray Muon Tomography
Using GEMs for Homeland security
Spin off is important key word for the HEP labs to survive …
Applications area will benefit from the technological developments developed by the RD51
The responsibility for the completion of the application projects lies with the institutes themselves
Technology
T2DM2: Temporal Tomography
Densitometric by the Measure of Muons
Liquid xenon detectors for functional medical imaging
Technology
CsI-RETGEM for UV
flame detection

## Slide 53
Focus on providing techniques for calculating electron transport in small-scale structures
The main difference with traditional gas-based detectors is that the electrode scale
(~ 10 mm) is comparable to the collision mean free path
WG4: MPGD Simulation Tools
Microscopic Tracking (Development and Maintenance of Garfield++): Garfield++ is a collection of classes for the detailed simulation of small-scale detectors.
Garfield++ contains: - electron and photon transport using cross sections provided by Magboltz - ionisation processes in gases, provided by Heed and MIP - ionisation and electron transport in semi-conductors - field calculations from finite elements, boundary elements, analytic methods Simulation Improvements:
 Transport:
- ion mobility and diffusion, measurement and modelling
- Magboltz cross sections (Ar, Xe, He, Ne; GeH4, SiH4, C2H2F4 ) are frequently
updated in collaboration with LXCAT (http://www.lxcat.laplace.univ-tlse.fr)
- e-ion recombination process in Xe
- thermal motion
 Photons:
- update in UV emission
- inclusion of IR production
- photon trapping and resulting excitation transport
- photon absorption in the gas (gas feedback)
- photon absorption in and electron emission from walls (feedback)
- photo cathodes

## Slide 54
WG4: MPGD Strong Simulation Efforts in Very Specific Needs
Applications:
GEM: multiplication process and polyimide properties; charging up effects
MicroMegas: timing and effects of resistive layers;
 ATLAS NSW upgrade: study of electron losses in MM with different mesh specifications
TPC GEM: ion backflow
 ALICE TPC upgrade: rate dependence of the Ion Back Flow in GEM
Measurement
Simulation

## Slide 55
WG4: GEM Charging-Up Effects Simulation
ANSYS: field model
Magboltz 9.0.1: relevant
cross sections of electron-matter interactions
Garfeld++: simulate
electron avalanches
Electric Field Intensity during
the charging-up process:
each iteration correspond to
the number of primary electrons that already reached to the hole
Charging effects are much smaller after (100 – 150) *105 avalanches
 GEM gas gain stabilizes

## Slide 56
Physical Overview of SRS:
Scalability from small to large system
Common interface for replacing the chip
frontend
Integration of proven and commercial
solutions for a minimum of development
Default availability of a very robust and
supported DAQ software package
WG5: The RD51 Scalable Readout System (SRS) for MPGD
RD51 Development / Industrialization: portable multi-channel readout system (2009-2012)
Scalable readout architecture: from ~ 100 channels up to very large LHC systems (> 100 k ch.)
Project specific part (ASIC) + common acquisition hardware and software
Frontend hybrids:
based on
APV25, VFAT, Beetle, VMMx and Timepix
chips
FEC cards (common):
Virtex-5 FPGA, Gb-Ethernet, DDR buffer, NIM and LVDS pulse I/O, High speed Interface connectors to frontend adapter cards
ADC frontend adapter
for APV and Beetle chips
ADC plugs into FEC to
make a 6U readout unit for
up to 2048 channels
Cheap! < 2 € / ch + FE
RD51 SRS is very successful  already used outside MPGD field (e.g. SiPM readout)
TODAY: # of SRS systems deployed ~ 100 with > 300 k APV channels,
total volume of SRS sales ~ 1 MCHF

## Slide 57
http://indico.cern.ch/event/356113/session/6/contribution/29/material/slides/1.pdf
SRS & APV25 FE chip
Worldwide use in the RD51 community (>2000 hybrids)
Very appealing for the future: VMM (NSW ATLAS FE chip)
SRS-FEC+TOTEM DAQ
SRS: Different System
SRS for R&D on Detectors
SRS for experiments (ATCA)
SRS for spatially distributed
system (optical SRS)
Baseline solution for RD51 SRS community.
Interest and support from ESS (European Spallation Source) and ALICE FOCAL
Continuously upgrading
Finalization of SRS ATCA
Half Done (started early 2014)
RD51 involvement since 2014
SRS+SiPM (NEXT TPC)
Ongoing – Baseline
Ongoing - scaled up
2015
SRS+Timepix (LC-TPC) – Bonn/Desy
Closed to commissioning in UCS
WG5: The RD51 Scalable Readout System (SRS) for MPGD
E. Oliveri

## Slide 58
https://indico.cern.ch/event/352483/
Construction of the new workshop’s building:
Start : beginning 2012
End: end 2017
New Capabilities….
MPGD Projects….
installation of the new infrastructure (to fabricate 2x1m2 Bulk MM & 2x0.5m2 GEM) COMPLETED
Antonio Teixeira
Interesting Workshop Overview Capabilities
OK
OK
OK
OK
OK
OK
WG6: MPGD Technology & Production @ CERN

## Slide 59
GEM Technology (contacts):
Mecharonix (Korea, Seoul)
Tech-ETCH (USA, Boston)
Scienergy (Japan, Tokyo)
TECHTRA (Poland, Wroclaw
THGEM Technology (contacts):
ELTOS S.p.A. (Italy),
PRINT ELECTRONICS
MicroMegas Technology(contacts):
ELTOS S.p.A. (Italy)
TRIANGLE LABS(USA, Nevada)
SOMACIS (Italy, Castelfidarco)
ELVIA (France, CHOLET)
GEM Licenses signed by:
Mecharonics, 21/05/2013
TECH-Etch, 06/03/2013
China IAE, 10/01/2012
SciEnergy, 06/04/2009
Techtra, 09/02/2009
CDT, 25/08/2008
PGE, 09/07/2007
Technology Industrialization  transfer “know-how” from CERN workshop to industrial partners
WG6: MPGD Technology Industrialization
GEM Industrialization Status (June 2015):
Micromegas Industrialization Status (June 2015):
ATLAS NSW upgrade  will first detector mass-produced in industry
using a large high-granularity Micromegas:
det. area ~1300 m2 divided into 2 m x 0.5 m2 units
TECH-ETCH
Single Mask process fully understood. Many 10cm x 10cm produced and characterized.
40cm x 40cm GEM successfully produced
CMS GE1/1 size of 1m x 0.5m started
TECHTRA
Production Line Operational
Stable process for 10cm x 10cm
Single Mask process completely understood – 10cm x 10cm produced
30cm x30cm Single Mask Produced
MECHARONICS
10cm x 10cm double mask produced and tested
30cm x 30cm double mask under evaluation @ CERN
CMS GE1/1 size of 1m x 0.5m started
ELVIA
Bulk Micromegas detectors are routinely produced with sizes up to 50cm x 50 cm.
Contract for ATLAS NSW module-0 signed
Tendering process for full production ongoing
ELTOS
Many small size bulk Micromegas detectors have been produced.
Contract for ATLAS NSW module-0 signed
Tendering process for full production ongoing

## Slide 60
Technical support
MPGD Detectors
Gas system and services
Readout electronics (std and custom RD51 SRS&APV)
Radioactive Sources
Interface with CERN services (RP, gas, metrology, irradiation facilities,…)
Permanent installations (Today): ALICE, ATLAS, ESS
CMS moved roughly two years ago to TIFF, access to the lab for specific measurements
More than 15/20 groups per year coming to perform measurements
Clean Rooms
Mechanical and Electronic Workshop
Continuously running…..” twenty-four seven”
WG7: PH-GDD Laboratory … Laboratory available for RD51 Collaboration
E. Oliveri

## Slide 61
2014 test Beam
CMS (GEM)
WIS/A/C(WELL, THGEM)
ATLAS NSW (mm)
BESS III & SHIP (GEM)
LAPP/DEM/IRFU(mm)
ALICE TPC (GEM and mm)
Building 887 – EHN1
H4 (PPE134)
Three periods of two weeks each per year
About fifteen-twenty users per year
Goliath Magnet (1.4 T)
 Ship Experiment?
December 2014
2008-2015: ~ 40 RD51 groups participated (2015 test Beam: May-June, July, October)
WG7:Semi-Permanent Test Beam Infrastructure in the SPS line
E. Oliveri

## Slide 62
October 2015 (Trieste)
2009
2011
2013
MPGD conferences & RD51CM
October 2014 (Kolkata)
IWAD conference &
RD51 Collaboration Meeting

## Slide 63
A fundamental boost is offered by RD51: from isolate MPGD developers to a world-wide net
A combined map of organizations working
with MPGDs built with collaboration-spotting software developed at CERN
 huge growth in interest in the MPGD
technologies
Collaboration Spotting Software:
http://collspotting.web.cern.ch/)
RD51 and the Rise of Micro-Pattern Gas Detectors
J.-M. Le Goff

## Slide 64
RD51 and the Rise of Micro-Pattern Gas Detectors
1998
2014
GEM
GEM
Micromegas:
Micromegas:
1998
2014
J.-M. Le Goff

## Slide 65
CERN Courier, October 2015

## Slide 66
Wire Chambers, TPC, RPC  MPGD (GEM, Micromegas)  InGrid (3D)
Micromegas:
Ingrid
TODAY:
FUTURE:
YESTERDAY:
INTEGRATION
INTEGRATION
Advances in photolithography 
Large Area MPGDs (~ m2 unit size)
High rate capability ~106 Hz/mm2
Spatial res. ~ 30-50 mm (TRACKING)
Time res. ~ 3-5 ns (TRIGGER)
LHC
HL-LHC
ILC
ILC
CLIC
Gaseous Tracking: Detector-Electronics Integration Trends

## Slide 67
Instead of Outlook … MPGD Performance Summary
MPGD Characteristics | Gas Electron Multipliers (GEM) | Micromegas/ Resistive MM
Active areas (Size of single detector module) / Large Scale Industrial Production | ~ 1 x 0.5 m2 yes | ~ 2 x 1 m2 yes
Radiation Hardness | > 10 HL-LHC years | > 10 HL-LHC years
High-Rate Capability | ~ 50 MHz/cm2 | Res MM (MHz/cm2): ~ 0.1 (today) ~ 10 - 50 (future)
Spatial resolution | <~30 mm (single layer) | <~30 mm (single layer) ang. dep.: mTPC
Tracking efficiency | 99% | 98%
Triggering efficiency (25 ns timing and B-field) | 95-98% | 95-98%
Timing Resolution | ~4-5 ns (MIP) & CF4 how to improve (?) | 3-5 ns (MIP) & CF4 how to improve (?)
MPGDs have also found numerous applications  they are being used or considered:
X-ray and neutron imaging, neutrino–nucleus scattering experiments, dark- matter
and astrophysics experiments, plasma diagnostics, material sciences, radioactive-waste
monitoring and security applications, medical physics and hadron therapy.